## Slide 1
Vlasov Sergey
smvlasov@itmo.ru
Цифровая и микроконтроллерная техника

## Slide 2: Analog to Digital Converter

## Slide 3: Dual Slope Analog to Digital Converter
Integrator

## Slide 4: Flash Analog to Digital Converter

## Slide 5: Successive Approximation Analog to Digital Converter
A sample-and-hold circuit to acquire the input voltage Vin.
An analog voltage comparator that compares Vin to the output of the internal DAC and outputs the result of the comparison to the successive-approximation register (SAR).
A successive-approximation register subcircuit designed to supply an approximate digital code of Vin to the internal DAC.
An internal reference DAC that, for comparison with Vref, supplies the comparator with an analog voltage equal to the digital code output of the SARin.

## Slide 6: Successive Approximation Analog to Digital Converter

## Slide 7: Sigma Delta Analog to Digital Converter

## Slide 8: ADC resolution vs Max sampling rate

## Slide 9: STM32 ADC

## Slide 10: STM32 ADC
A/D conversion can be:
Single Conversion. One sample conversion at a given instant.
Continuous Conversion. Non-stop sample collection and conversion.
Discontinuous Conversion. Sequential conversion of some channels in a group.
Scan Conversion. Sequential sampling and converting of an array of channels one after another.
To start A/D conversion, an ADC unit needs to be stimulated with a trigger signal:
Software Trigger. A/D conversion as per demand from coded program.
Hardware Trigger. A/D conversion as per hardware events like external interrupts or timer events.

## Slide 11: Timing diagram

## Slide 12: ADC Groups

## Slide 13: Conversion on external trigger and trigger polarity

## Slide 14: ADC with DMA

## Slide 15: ADC registers
ADC status register (ADC_SR)
ADC control register 1,2 (ADC_CR1,2) ADC sample time register 1,2 (ADC_SMPR1,2)
ADC injected channel data offset register x (ADC_JOFRx) (x=1..4)
ADC watchdog higher/lower threshold register (ADC_{H/L}TR)
ADC regular sequence register 1,2,3 (ADC_SQR1,2,3)
ADC injected sequence register (ADC_JSQR)
ADC injected data register x (ADC_JDRx) (x= 1..4)
ADC regular data register (ADC_DR)
ADC Common status register (ADC_CSR)
ADC common control register (ADC_CCR)
ADC common regular data register for dual and triple modes (ADC_CDR)

## Slide 16: ADC registers
ADC status register (ADC_SR)
Address offset: 0x00
AWD: Analog watchdog flag
0: No analog watchdog event occurred
1: Analog watchdog event occurred
EOC: Regular channel end of conversion
0: Conversion not complete (EOCS=0), or sequence of conversions not complete (EOCS=1)
1: Conversion complete (EOCS=0), or sequence of conversions complete (EOCS=1)
STRT: Regular channel start flag
0: No regular channel conversion started
1: Regular channel conversion has started
OVR: Overrun
0: No overrun occurred
1: Overrun has occurred

## Slide 17: ADC registers
ADC control register 1 (ADC_CR1)
Address offset: 0x04
AWD: Analog watchdog flag
0: No analog watchdog event occurred
1: Analog watchdog event occurred
EOC: Regular channel end of conversion
0: Conversion not complete (EOCS=0), or sequence of conversions not complete (EOCS=1)
1: Conversion complete (EOCS=0), or sequence of conversions complete (EOCS=1)
STRT: Regular channel start flag
0: No regular channel conversion started
1: Regular channel conversion has started
OVR: Overrun
0: No overrun occurred
1: Overrun has occurred

## Slide 18: Example schematic
ADC
Timer
TRIG
IN0..15
DMA
Request
Data
Memory
DMA
USART
DMA TC Interrupt Handler
Software
Start transfer
Data
to PC
IRQ

## Slide 19: Algorithm
Enable ADC and config required GPIO pins.
Config ADC:
  Set work with DMA.
  Set start convert by external trigger and choose trigger source.
  Set scan mode.
  Set number of converting and queue.
Config timer for create trigger event on update.
Config DMA stream for ADC and enable interrupt on TC.
Config USART and DMA for Transmit function.
In DMA IRQ Handler config buffer and start transmission by enabling DMA.
Steps of initialization system

## Slide 20: ADC Data alignment

## Slide 21: DMA Example
int main()
{ ADC1->CR2 = ADC_CR2_ADON | // Enable ADC
ADC_CR2_DMA | ADC_CR2_DDS | // Enable DMA access
ADC_CR2_EXTEN_0 | // Enable external trigger
ADC_CR2_EXTSEL_X; // Choose external trigger
ADC1->CR1 = ADC_CR1_SCAN; // Set scan mode
ADC1->SQR1 = (NUMBER_OF_CONV - 1) << ADC_SQR1_L_POS;//Set numb of conventions
ADC1->SQR3 = NUMBER_OF_CHANNEL << ADC_SQR3_SQ1_POS | //Set channels queue
NUMBER_OF_CHANNEL << ADC_SQR3_SQ2_POS …;
… //Timer init
TIMX->CR2 |= TIM_CR2_MMS_1; // Enable triggering
…
DMA1_Stream6->CR = DMA_SxCR_CIRC | // Set DMA circ mode
      DMA_SxCR_MINC | // Set memory increase mode
DMA_SxCR_MSIZE_0 | // Set memory size to 16-bit
DMA_SxCR_PSIZE_0 | // Set peripheral size to 16-bit
DMA_SxCR_TC; // Enable interrupt on TC
DMA1_Stream6->NDTR = NUMBER_OF_CONV;
// Enable DMA
}

## Slide 22: Servo for control

## Slide 23: Final system schematic
PLANT
Motor with gears
and potentiometer
( 5-wire servo)
H-bridge
STM32
ADC
Timer
PID
u

## Slide 24: PID

## Slide 25: Thank you for attention
www.ifmo.ru